90W Universal Notebook/MP3 AC Adapter w/USB LCD Display & 8 LShaped Power Tips for Acer HP Dell Toshiba Sony & More

Part # LS-PAB90-BC10-A-H-L

Don't bother carrying around multiple power chargers for your mobile electronics. With this 90-Watt Multi-Functional Notebook/MP3 AC Adapter, you can charge your laptop, MP3 player, mobile phone and more!

That's because this universal adapter features a USB port for connecting any device that can charge via USB. That includes iPods and digital cameras, too! In addition, it comes with 8 different L-shaped connector tips that are compatible with notebooks from today's most popular brands, from HP, Compaq, Sony, Gateway, Acer to Toshiba. Since it has an input voltage of 100-240 volts, it is compatible worldwide, and features a maximum output of 9.5-22 volts (90 watts).

The LCD display shows the charging and power status with red and blue backlighting. Leave your power woes behind, order this handy 90-Watt Multi-Functional Notebook/MP3 AC Adapter today!

--------------------------------------------------------------------------------

Features/Specifications:

90-Watt Multi-Functional Notebook/MP3 Player AC Adapter

--------------------------------------------------------------------------------

General Features:

Color: Silver

LCD screen displays the charging and power status with red and blue colors

Advanced MCU microcomputer chip control

USB port for charging MP3 players, mobile phones, digital cameras, camcorders, and any other devices with USB

Worldwide compatibility (Input: 100-240V)

Automatic switching

100,000 level of anti-static design, high temperature and fire-proof crust makes it safer

--------------------------------------------------------------------------------

Power Specifications:

Input: 100-240V ~ 1.8A, 50/60Hz

Output: 9.5-22V, 5A (max) 90W

USB: 5V, 1A (max) 5W

--------------------------------------------------------------------------------

Tip Specifications:

Tip A:

Output voltage: 19V

Range voltage: 18.1-19.9V

Output current (max): 4.74A

Compatible with: HP/Compaq: 18.5V/2.7A, 18.5V/3.5A, 18.5V/3.8A, 18.5V/4.9A; Delta: 19V/2.64A; Asus: 19V/2.64A; NEC: 19V/2.64A

Tip B:

Output voltage: 15V

Range voltage: 14.3-15.7V

Output current (max): 5A

Compatible with: Toshiba: 15V/3A, 15V/4A, 15V/5A, 15V/6A; NEC: 15V/6A

Tip C:

Output voltage: 19V

Range voltage: 18.1-19.9V

Output current (max): 4.74A

Compatible with: Acer: 19V/3.16A, 19V/3.42A, 19V/4.74A; Lite-On: 19V/3.16A, 19V/3.42A; NEC: 19V/3.16A

Tip D:

Output voltage: 19V

Range voltage: 18.0-19.9V

Output current (max): 4.74A

Compatible with: IBM: 19V/4.2A; Dell: 19V/3.16A, 19V/3.42A; Compaq/HP: 18.5V/4.9A, 19V/4.9A; Delta: 19V/2.64A; Toshiba: 19V/3.16A, 19V/3.42A, 19V/4.74A; NEC: 19V/2.64A, 19V/3.16A; Lite-On: 19V/3.16A, 19V/3.42A, 19V/3.95A, 19V/4.74A; Gateway: 19V/3.16A, 19V/3.42A, 19V/4.74A; Asus: 19V/4.74A; LS: 20V/3.25A

Tip E:

Output voltage: 16V

Range voltage: 15.2-16.8V

Output current (max): 5A

Compatible with: IBM: 16V/2.2A, 16V/3.36A, 16V/3.5A, 16V/4.5A

Tip F:

Output voltage: 19V

Range voltage: 18.1-19.9V

Output current (max): 4.74A

Compatible with: Samsung: 19V/3.16A, 19V/3.75A, 19V/4.22A, 19V/4.74A

Tip G:

Output voltage: 16V

Range voltage: 15.2-16.8V

Output current (max): 5A

Compatible with: Sony: 16V/3.42A, 16V/3.75A, 16V/4A; Fujitsu: 16V/3.36A, 16V/3.75A

Tip H:

Output voltage: 19.5V

Range voltage: 18.5-20.4V

Output current (max): 4.62A

Compatible with: Sony: 19.5V/2.7A, 19.5V/3A, 19.5V/4.1A, 19.5V/4.7A; Fujitsu: 19V/3.16A, 19V/3.69A, 19V/4.22A

--------------------------------------------------------------------------------

Regulatory Approvals:

FCC

CE

UL

C-Tick

WEEE

--------------------------------------------------------------------------------

Package Includes:

90-Watt Multi-Functional Notebook/MP3 Player AC Adapter

Eight (8) connector tips (A-H)

Power cord

User guide

--------------------------------------------------------------------------------

Additional Information:

Product Requirements:

Available power outlet

Compatible laptop/notebook

Compatible USB device